## Slide 1: Unit-5 Combinational Circuit Adders Subtractor Decoder-Encoder Multiplexers-Demultiplexers Comparator Parity Generators

## Slide 2: Combinational Circuits
Output depends only on the present input
The combinational circuit do not use any memory.
The previous state of input does not have any effect on the present state of the circuit.

## Slide 3: 1. Half Adder
A combinational logic circuit with two inputs and two outputs.
The half adder circuit add two single bit Cary number
This circuit has two outputs carry and sum.
S(A, B) = ∑m (1, 2)
CY(A, B) = ∑m (3)

## Slide 4: 2. Full Adder (1-bit Adder)
A combinational logic circuit with 3 inputs and 2 outputs.
The Full adder circuit add 3 single bit Cary number
This circuit has two outputs carry and sum.

## Slide 5
For Cout
Cout=AB+BC+AC

## Slide 6: Full Adder using Half Adder
FA
Sum= A⊕B⊕C
Carry=AB+(A⊕B)C
HA
Sum= A⊕B
Carry=AB

## Slide 7: 3. Half Subtractor
Combinational circuit perform binary Subtraction
Accepts 2 input and Two output Difference and Borrow

## Slide 8: 4. Full Subtractor
Performs subtraction of 3 bits
This circuit has three inputs and two outputs.
The three inputs A, B and C, denote the minuend, subtrahend, and previous borrow, respectively.
The two outputs, D and Bout
F(A, B,C) = ∑m (1, 2, 4, 7)
Bout(A, B,C) = ∑m (1,2,3,7)

## Slide 9
Bout = A’B’C + A’BC’ + A’BC + ABC
= C(AB + A’B’) + A’B(C + C’)
= C( A XNOR B) + A’B
= C (A XOR B)’ + A’B

## Slide 10: Full Subtractor using Half Subtractor
FS
Difference= A⊕B⊕C
Borrow=A’B+(A⊕B)’C
HS
Difference= A⊕B
Borrow=A’B

## Slide 11: 5. 1-BIT Magnitude Comparator
1-Bit Magnitude Comparator
A
B
GT
EQ
LT
GT
EQ
LT
GT=AB’
EQ=A’B’+AB
LT=A’B

## Slide 12: 6. 2-BIT Magnitude Comparator

## Slide 13: 7. Multiplexer
A combinational circuit has maximum of 2n data inputs, ‘n’ selection lines and single output line.
One of these data inputs will be connected to the output based on the values of selection lines
It is a data selector device
Size of multiplexer is :1
2:1 Multiplexer
I0
I1
Y
S
=S’I0 + SI1
0
1

## Slide 14: 4:1 Multiplexer
Selection Lines |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3

## Slide 15: 8. Demultiplexer
switch one common input line to one of several output line based on select input
It is data distributor
Size of demux 1: Example 1:4, 1:8, 1:16….. Demultiplexer
Selection Inputs |  | Outputs |  |  | 
S1 | S0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | I
0 | 1 | 0 | 0 | I | 0
1 | 0 | 0 | I | 0 | 0
1 | 1 | I | 0 | 0 | 0

## Slide 16: 9. Decoder
A combinational circuit that has ‘n’ input lines and maximum of 2n output lines.
One of these outputs will be active High based on the combination of inputs present, when the decoder is enabled.
The outputs of the decoder are min terms of ‘n’ input variables lines when it is enabled
Size of Decoder are 2:4, 3:8, 4:16….
A1 | A0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0

## Slide 17: 10. 4:2 Encoder

## Slide 18: 11. Parity Generator Circuit
Even Parity Generator
If odd number of ones present in the input, then even parity bit, P should be ‘1’ so that the resultant word contains even number of ones.
Binary Input WXY | Even Parity bit P
000 | 0
001 | 1
010 | 1
011 | 0
100 | 1
101 | 0
110 | 0
111 | 1
Odd Parity Generator
If even number of ones present in the input, then odd parity bit, P should be ‘1’ so that the resultant word contains odd number of ones
Binary Input WXY | Odd Parity bit P
000 | 1
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 0