## Slide 1: ECE249
UNIT-2
Lecture 2

## Slide 3: Transistor Construction
Figure NPN transistor.

## Slide 4
Emitter is ................. Doped
QUIZ POLL
heavily
lightly
Medium
All of the above

## Slide 5
Figure PNP transistor.

## Slide 6
Emitter is ................. Doped
QUIZ POLL
heavily
lightly
Medium
All of the above

## Slide 7
In a pnp transistor, the current carriers are ………….
acceptor ions
donor ions
free electrons
holes

## Slide 8
In a npn transistor, ……………. are the minority carriers
free electrons
holes
donor ions
acceptor ions

## Slide 9
Collector has ............... size among all terminals in BJT
QUIZ POLL
least size
Medium
biggest
All of the above

## Slide 10
The element that has the smallest size in a transistor is ………………..
QUIZ POLL
collector
base
emitter
collector-base-junction

## Slide 11: BIPOLAR JUNCTION TRANSITOR (BJT)
Transistor is a solid state device
It is a current controlled device
It has three terminals
  Emitter
  Base
  Collector
There are two types of Transistor
  PNP
  NPN
Doping of Terminals
  Emitter- highly doped
  Base- Lightly doped
  Collector- Moderately doped

## Slide 12: Transistor wrt Vaccum Triode
  Advantages
Compact Size
Light weight
Rugged Construction
Resistive to shock and vibration
Instantaneous operation
High operation point
Long life
No aging effect
  Disadvantages
Loud hum noise
Restricted operation up to 75 degree
Operating frequency – Few MHz

## Slide 24
At the emitter base junctions of a transistor, one finds………….
A reverse bias
A wide depletion layer
Low resistance
Both a and b

## Slide 25
Most of the majority carriers from the emitter……………
Most of the majority carriers from the emitter……………
QUIZ POLL
Recombine in the base
Recombine in the emitter
Pass through the base region to collector
Both a and b
Both b and c
Recombine in the base
Recombine in the emitter
Pass through the base region to collector
Both a and b
Both b and c